LAB-4>Network Data Analysis using tcpdump

1. While tcpdump host your_host is running in one command window, run ping 127.0.0.1 from
another command window. From the ping output, is the 127.0.0.1 interface on? Can you see any
ICMP message sent from your host in the tcpdump output? Why?

-> Since, we use ping and it remains in the localhost, we cannot detect it in the tcmp output.
Network stack ignores loopback as local traffic since it doesn’t go through the network.

2. While tcpdump host your_host is running to capture traffic from your machine, execute telnet
128.238.66.200. Note there is no host with this IP address in the current configuration of the lab
network. Save the tcpdump output of the first few packets for the lab report. After getting the
necessary output, terminate the telnet session. From the saved tcpdump output, describe how the
ARP timeout and retransmission were performed. How many attempts were made to resolve a
non-existing IP address?

Ping to non existent ip address 172.16.59.69 . The source makes three attempts to get a	response (mac address and other details) from the device at the address. However since it is	non existent, it gets no response.

3. Briefly explain the purposes of the following tcpdump expressions.

a. tcpdump udp port 520
filters captured UDP packets output for port 520 which is reserved for Routing Information	Protocol

b. tcpdump -x -s 120 ip proto 89
filters captured IP packets with protocol number 89 (which corresponds to Open Shorted	Path First (OSPF) used in IP networks) and displays it in hexadecimal/ ASCII format with	snapshot length 120 bytes

c. tcpdump -x -s 70 host ip addr1 and (ip addr2 or ip addr3)
To capture communication between specific hosts. filters captured IP packets for ip	addresses ip addr1, addr2 or ip addr3 in hexadecimal/ASCII format with snapshot	length 70 bytes.

d. tcpdump -x -s 70 host ip addr1 and not ip addr2
To capture all packets for the host ip addr1 excluding the ip addr 2 in hexadecimal/ASCII	format with snapshot length 70 bytes.

4. Basic packet decoding
1) Write a tcpdump command to dump network traffic from an Ethernet connection to the screen in human readable output format. Perform the following operation and write down the observations.
a) Capture all the traffic of maximum snap length of 65,535 bytes and provide the
hexadecimal and ASCII decodes of all the traffic in each packet.

sudo tcpdump -x -c 1 -tttt -v -s 65535

sudo: superuser privileges
-c 1: Capture first packet
-x: hex/ascii format
-tttt: Provides human readable detailed timing information
-v: verbosity
-s 65535: snapshot length 65535

b) Find the IP addresses, IP packet length, TCP port numbers, TCP flags, etc. by using
the reference chart to locate those fields on the hexadecimal dump.

tcpdump: listening on wlp0s20f3, link-type EN10MB (Ethernet), snapshot length 65535 bytes
2023-08-31 19:55:45.259784 IP6 (flowlabel 0x7db08, hlim 64, next-header TCP (6) payload length: 56) satwik-mint.47992 > 2405:200:1608:1731::17c1:3812.https: Flags [P.], cksum 0xf8a8 (incorrect -> 0x4d09), seq 1806427138:1806427162, ack 1056291480, win 5203, options [nop,nop,TS val 3170606680 ecr 803247281], length 24
0x0000: 6007 db08 0038 0640 2405 0201 d014 88f7
0x0010: 7f75 3c1a 2ab9 effd 2405 0200 1608 1731
0x0020: 0000 0000 17c1 3812 bb78 01bb 6bab e402
0x0030: 3ef5 ba98 8018 1453 f8a8 0000 0101 080a
0x0040: bcfb 9e58 2fe0 94b1 1703 0300 131b 83ba
0x0050: 1702 01ba 2c20 7515 407c 5ce6 c173 2ce0
1 packet captured
28 packets received by filter
0 packets dropped by kernel