Analyzing UDP datagrams using wireshark

A. In the packet list pane, select the first DNS packet. In the packet detail pane, select the
User Datagram Protocol. The UDP hexdump will be highlighted in the packet byte lane.
Using the hexdump, Answer the following:
a. the source port number.
47291

b. the destination port number.
 53

c. the total length of the user datagram.
60
d. the length of the data.

40

e. whether the packet is directed from a client to a server or vice versa.
Client to server
f. the application-layer protocol.
User datagram protocol
g. whether a checksum is calculated for this packet or not.

B. What are the source and destination IP addresses in the DNS query message? What are those
addresses in the response message? What is the relationship between the two?

In the response HTTP message, the address are the opposite i.e. source becomes the destination anf the previous destination becomes the source.

C. What are the source and destination port numbers in the query message? What are those
addresses in the response message? What is the relationship between the two? Which port
number is a well-known port number?
QUERY:	src: 47291	dst: 53
RESPONSE	src: 53	dst:47291
53 is the standard port for DNS

D. What is the length of the first packet? How many bytes of payload are carried by the first
packet?
Length: 40
UDP Payload: 202 bytes

FLAGS:

SYN, SYN-ACK, ACK

1. What are the socket addresses for each packet?
SYN: Source: 10.86.2.232:54980 Destination: 8.8.4.4:443
SYN-ACK: Source: 8.8.4.4:443 Destination: 10.86.2.232:54980
ACK: Source: 8.8.4.4:443 Destination: 10.86.2.232:54980

2. What flags are set in each packet?
0X002 : SYN flag is set
0x012: SYN and ACK flags are set
0x010: ACK flag is set

3. What are the sequence number and acknowledgment number of each packet?

SYN: Seq Number: 3791519344, Ack Number: 0
SYN-ACK: Seq Number: 3897095971, Ack Number: 3791519345
ACK: Seq Number: 3987100586, Ack Number: 3971307332

4. What are the window size of each packet?
SYN: 74220
SYN-ACK: 75445
ACK: 81850

Part II: Data-Transfer Phase
The data-transfer phase starts with an HTTP GET request message and ends with an HTTP OK
message.

1. What TCP flags are set in the first data-transfer packet (HTTP GET message)?
ACK and PUSH flags

2. How many bytes are transmitted in this packet?
87 bytes
3. How often does the receiver generate an acknowledgment? To which acknowledgment rule
(defined in Page 200 in the textbook) does your answer correspond to?
0.053926

4. How many bytes are transmitted in each packet? How are the sequence and acknowledgment
numbers related to number of bytes transmitted?
87 bytes transmitted in GET request, 154 bytes recieved in response.
Sequence numbers increases as number of bytes transmitted increase.

5. What are the original window sizes that are set by the client and the server? Are these numbers
expected? How do they change as more segments are received by the client?

Window size will increase as long as hardware supports it to reduce congestion.

6. Explain how the window size is used in flow control?
Sender can only send bytes that can fit in the reciever’s buffer then must wait till the bytes	have been acknowledged to prevent congestion in turn improving flow control.

7. What is the purpose of the HTTP OK message in the data transfer phase?
OK mesage means that the request succeeded

Part III: Connection Termination Phase
The data-transfer phase is followed by the connection termination phase. Note that some packets
used in the connection-termination phase may have the source or sink protocol at the application
layer. Find the packets used for connection termination.

1. How many TCP segments are exchanged for this phase?
4 segments are exchanged in the connection termination phase. (FIN, ACK, FIN, ACK)
2. Which end point started the connection termination phase?
Server
3. What flags are set in each of segments used for connection termination?
Segment 1 Client sends FIN flag to server to initiate termination indicating end of data	sending process
Segment 2 : Server sends ACK flag to client to acknowledge FIN flag reception
Segment 3 (Server to Client):FIN flag
Segment 4 (Client to Server): ACK flag to indicate completion of termination process